# Lotus Exige S Technical Specifications, Exterior & Interior Specifications, Options

| Vehicle Description | Technical Specification |
| --- | --- |
|  | Lotus Exige S |
| Engine | Mid-mounted, transverse, 3456 cm3, 2GR-FE engine, aluminium lightweight and compact construction, V6 24 valve, water cooled, supercharged with double overhead camshafts per cylinder bank, 4 valves per cylinder, Dual-Variable Valve Timing – intelligent, direct ignition system, electronic throttle control system-intelligent Harrop HTV 1320 supercharger assembly (utilising Eaton Twin Vortex Series (TVS) Technology ™) |
| Engine management | Lotus T6e engine control unit |
| Compression Ratio | 10:1 |
| Bore x Stroke | 94 x 83 |
| Max Power | 350 PS / 257.5 kW / 345 hp @ 7000 rpm |
| Max Torque | 400 Nm / 295 lb ft @ 4500 rpm |
| Emissions control | Three-way catalytic converter. Euro V emissions compliant with full On-Board Diagnostics (OBD). |
| Transmission | EA60 6 speed transverse Sports Ratios manual gearbox with open differential |
| Suspension | Fully independent suspension utilizing unequal length wishbones, Bilstein mono-tube gas damper, Eibach coaxial coil spring at each corner and front and rear anti-roll bar. |
| Chassis | Lotus designed lightweight structure of epoxy bonded aluminium alloy extrusions with integral steel seat-belt support structure and lightweight steel rear subframe. |
| Dynamic Performance Management (DPM) | Corner Brake Control (CBC) Drag Torque Control (DTC) Electronic Differential Lock (EDL) Traction Control System (TCS) Electronic Stability Control (ESC) Anti-lock Braking System (ABS)* Hydraulic Brake Assist (HBA)* Electronic Brake Distribution (EBD)* Understeer Recognition All apart from * can be completely switched off DPM with Sports Mode button Sport Mode increases the traction slip thresholds and removes understeer recognition, allowing the driver more vehicle control before an intervention is required. |
| Steering | Solidly mounted mechanical rack and pinion steering box with 2.8 turns lock-to-lock. |
| Brakes | Servo-assisted, track tuned 4-channel Antilock Braking System (ABS) AP-Racing four-piston calipers (front and rear) Front: 350 mm ventilated and cross drilled cast-iron discs Rear: 332 mm ventilated and cross drilled cast-iron discs |
| Wheels Front Rear | Lightweight alloy wheels 17” 18” |
| Tyres Front Rear | Pirelli P-Zero Corsa 205/45 R17 265/45 R18 |
| Gear ratios | 1st: 3.538 2nd: 1.913 3rd: 1.407 4th: 1.091 5th: 0.9697 6th: 0.8611 Reverse: 3.831 Final Drive (1st-4th): 3.777 Final Drive (5th – 6th) 3.238 |

| Target Performance Figures (Subject to Type Approval and Subject to Change) |  |
| --- | --- |
| Max. Engine Speed | 6,600 rpm continuous and 6,800 rpm transient 7,000 rpm continuous and 7,200 rpm transient (Sport Mode) |
| 0-100 km/h | ~ 3.8 seconds |
| 0-160 km/h) | 7.9 seconds |
| Maximum speed | ~274 km/h / ~170 mph |
| Fuel tank capacity | 40 litres ( 8.8 gal (UK) ) |

| Dimensions |  |
| --- | --- |
| Wheelbase | 2370 mm |
| Track – front | 1453 mm |
| Track – rear | 1499 mm |
| Overall length | 4052 mm |
| Overall width (door mirrors excluded) | 1802 mm |
| Overall height – midladen (as per unladen with 2x 75 kg occupants) | 1153 mm |
| Overhang – front (including splitter) | 880 mm |
| Overhang – rear | 802 mm |
| Ramp Angle – front | 7.4 degrees |
| Ramp Angle – rear | 16.4 degrees |
| Ground clearance – midladen (as per unladen with 2x 75 kg occupants) | 130 mm (front); 135 mm (rear) |
| Target Vehicle mass – kerb | 1,080 kg |
| Drag Coefficient | 0.433 |

| Exterior Specification |  |
| --- | --- |
| Solid paint | S |
| Metallic paint | O |
| Premium paint | O |
| Motorsport paint | O |
| Satin black wheels, cast (17” front and 18” rear) | S |
| Diamond cut wheels, cast (17” front and 18” rear) | O |
| Pirelli P-Zero Corsa tyres Front: 205/45 R17 & Rear: 265/45 R18 | S |
| Pirelli P-Zero Trofeo tyres Front: 205/45 R17 & Rear: 265/45 R18 | O |

| Interior Specification |  |
| --- | --- |
| Lightweight aluminium passenger footrest | S |
| Lightweight aluminium footwell divider | S |
| Driver and passenger airbags | S |
| Black leather steering wheel | S |
| Black leather gear lever gaiter | S |
| Polished aluminium gear knob | S |
| Plain leather sun-visors | S |
| Black carpet mats | S |
| Black seats with Lotus roundel | S |
| Contrast stitching (Premium Pack Sport SuedeTex® required) | O |
| CD/MP3/WMA receiver with 4 speakers | S |
| Immobiliser and remote activated alarm | S |
| Central door locking | S |
| Engine start push button | S |
| Rear parking sensors | O |
| Heated seats | O |
| Face-level air vents | S |
| Air conditioning | O |
| Crossbar and harness mounts | O |

| Option Packs |  |
| --- | --- |
| Premium Pack Choice of leather colour: Ebony Black, Ivory White, Venom Red, Cognac Brown, Imperial Blue, Cocoa Brown, Ash Grey Leather centre console Fully covered foot well area (carpet + leather) Sport/Premium steering wheel in full black leather leather sills Door panels in leather Metal bezel around gear and handbrake gaiter Sport/Premium seats in full leather Full sound insulating material Dark trinket tray Face-level air vents covered in leather | O |
| Premium Pack Sport SuedeTex® Ebony Black/Slate Grey SuedeTex® interior combination, SuedeTex® centre console Black floor mats Sport/Premium steering wheel with dark grey leather Dark grey binnacle top, Door panels in carbon effect leather Metal bezel around gear and handbrake gaiter Sport/Premium seats with carbon effect eather inserts Sound insulating material | O |
| Carbon Pack (Premium Pack required) Carbon centre console Carbon sill covers Carbon air conditioning controls Carbon air conditioning vents Carbon binnacle surround and binnacle top Carbon Dynamic Performance Management (DPM) switch panel | O |
| Race Pack 4 mode Lotus DPM system including launch control Exhaust bypass valve override switch Optimised suspension to suit the Pirelli P-Zero Trofeo tyre characteristics | O |
| Convenience Pack Trinket tray divider USB connection cup holder | O |

S = Standard						N/A = Not Available

O = Optional						POA = Price On Application.

* iPod is a trade mark of Apple Inc registered in USA and other countries.