|  | Hyundai Motor America 10550 Talbert Ave., Fountain Valley, CA 92708 TEL: 714-965-3000 FAX: 714-378-1008 MEDIA WEBSITE: HyundaiNews.com CORPORATE WEBSITE: HyundaiUSA.com |  |
| --- | --- | --- |
|  | 2014 Genesis Coupe |
| ENGINE |
| 2.0T |
| Type | Front-mounted, intercooled-turbocharged 2.0L DOHC Dual CVVT (Dual Continuously Variable Valve Timing) |
| Materials | All aluminum |
| Bore & Stroke | 86 mm x 86 mm |
| Displacement | 2.0 liters |
| Horsepower | 274 @ 6,000 rpm (premium) 260 @ 6,000 rpm (regular) |
| Torque | 275 lb-ft @ 2,000 rpm (premium) 260 lb-ft @ 2,000 rpm (regular) |
| Valves per cylinder | 4 |
| Compression Ratio | 9:1 |
| Top Speed | 146 mph, fuel cut |
| 3.8 |
| Type | 3.8L DOHC GDI V6 Dual CVVT (Dual Continuously Variable Valve Timing) |
| Materials | All aluminum |
| Bore & Stroke | 96 mm x 87 mm |
| Displacement | 3.8 liters |
| Horsepower | 348 @ 6,400 rpm (premium) 344 @ 6,400 rpm (regular) |
| Torque | 295 lb-ft @ 5,100 rpm (premium) 292 lb-ft @ 5,100 rpm (regular) |
| Valves per cylinder | 4 |
| Compression Ratio | 11.5:1 |
| Top speed | 149 mph, fuel cut |
| TRANSMISSION |
| 2.0T, 6-speed manual with carbon synchronizers / 8-speed automatic with lockup torque converter & paddle-shift SHIFTRONIC® |
| Gear ratios | 6MT / 8AT |
| First | 3.848 / 3.964 |
| Second | 2.317 / 2.468 |
| Third | 1.623 / 1.610 |
| Fourth | 1.233 / 1.176 |
| Fifth | 1.000 / 1.000 |
| Sixth | 0.794 / 0.832 |
| Seventh | -- / 0.652 |
| Eighth | -- / 0.565 |
| Reverse | 3.985 / 2.273 |
| Final drive | 3.727 / 4.181 |
| 3.8, 6-speed manual / 8-speed automatic with lockup torque converter & paddle-shift SHIFTRONIC® |
| Gear ratios | 6MT / 8AT |
| First | 3.848 / 3.964 |
| Second | 2.317 / 2.468 |
| Third | 1.623 / 1.610 |
| Fourth | 1.233 / 1.176 |
| Fifth | 1.000 / 1.000 |
| Sixth | 0.794 / 0.832 |
| Seventh | -- / 0.652 |
| Eighth | -- / 0.565 |
| Reverse | 3.985 / 2.273 |
| Final drive | 3.538 / 3.909 |
| SUSPENSION |
| Front | Sport-tuned MacPherson strut dual link with springs, gas charged shock absorbers and 23 mm stabilizer bar (Standard) Track-tuned springs, gas charged shock absorbers and 24 mm stabilizer bar (R-Spec/Ultimate) |
| Rear | Sport-tuned five-link design with monotube gas charged shock absorbers and 19 mm stabilizer bar (Standard) Track-tuned springs, monotube gas charged shock absorbers and 20 mm stabilizer bar (R-Spec/Ultimate) |
| STEERING |
| Type | Rack-and-pinion, hydraulic power assisted |
| Overall Ratio | 13.8:1 |
| Turning circle, diameter | 37.4 ft |
| Turns, lock to lock | 2.7 |
| BRAKES/TIRES/WHEELS |
| Front | 12.6-in. ventilated rotors, single piston floating calipers (Standard) 13.4-in. disc, 4-piston calipers (R-Spec/Ultimate) |
| Rear | Solid rotors, 12.4-inch, single piston floating calipers (Standard) 13.0-inch disc, 4-piston calipers (R-Spec/Ultimate) |
| ABS | 4-channel ABS with Electronic Brake-force Distribution (EBD) |
| All Season Tires | Front: 225/45VR18 Rear: 245/45VR18 |
| Summer Tires | Front: 225/40VR19 (R-Spec/ Ultimate) Rear: 245/40VR19 (R-Spec/ Ultimate) |
| Wheels | 18-inch alloy wheels 19-inch alloy wheels (R-Spec/Ultimate) |
| EXTERIOR DIMENSIONS |
| Wheelbase | 111.0 in. |
| Overall length | 182.3 in. |
| Overall width | 73.4 in. |
| Overall height | 54.5 in. |
| Overhang (front) | 32.9 in. |
| Overhang (rear) | 38.4 in. |
| Track, front | 63.0 in. |
| Track, rear | 63.6 in. |
| Minimum ground clearance | 5.1 in. |
| Coefficient of drag (Cd) | 0.32 |
| INTERIOR DIMENSIONS |
| Head room |
| Front | 39.2 in. |
| Rear | 34.6 in. |
| Leg room |
| Front | 44.1 in. |
| Rear | 30.3 in. |
| Shoulder room |
| Front | 56.7 in |
| Rear | 52.8 in |
| Hip room |
| Front | 56.0 in |
| Rear | 49.2 in |
| EPA passenger volume | 88.8 cubic ft. |
| EPA cargo volume | 10.0 cubic ft. |
| EPA total volume | 98.8 cubic ft. |
| CAPACITIES |
| 2.0T/3.8 |
| Fuel | 17.2 gallons |
| Oil | 6.5 liters |
| CURB WEIGHT |
| 2.0T manual / automatic | 3,455 / 3,495 lbs. |
| 3.8 manual / automatic | 3,503 / 3,594 lbs. |
| FUEL ECONOMY | City | Highway | Combined |
| 2.0T |
| 2.0T-liter manual | 19 mpg | 27 mpg | 22 mpg |
| 2.0T-liter automatic | 17 mpg | 27 mpg | 21 mpg |
| 3.8 |
| 3.8-liter manual | 16 mpg | 24 mpg | 19 mpg |
| 3.8-liter automatic | 16 mpg | 25 mpg | 19 mpg |

\