Media Information – Specifications

Infiniti Q80 Inspiration powertrain, chassis and interior specifications

| Q80 Inspiration | Exterior dimensions (millimetres) | Exterior dimensions (inches) |
| --- | --- | --- |
| Length | 5060 | 199.2 |
| Wheelbase | 3070 | 120.9 |
| Width | 2010 | 79.1 |
| Height | 1340 | 52.8 |

| Q80 Inspiration | Body / chassis highlights |
| --- | --- |
| Body type / size | Fastback / full-size, luxury |
| Construction materials | Aluminium / carbon fibre / chrome trim |
| Active components | Shutter front grille |
| Doors number / type | Four / Portal-style |
| Headlights type | Computer-controlled, directional full LED |
| Taillights type | Full LED |
| Exterior cameras number / type | Five / full colour, low-light enhanced, radar-linked |
| Paint color / type | Inspired Silver / UV and scratch resistant |
| Chassis type | Carbon fibre / aluminium monocoque |
| Powertrain layout | Front mount engine / motor, rear drive with all-wheel drive |
| Steering | Drive-by-wire, front axle |
| Wheels | 22-inch, 5-axis milled lightweight aluminium alloy wheels |
| Exhaust system | Custom fabricated stainless steel system with quad tailpipes integrated into the rear splitter. Internal pipework milling for soundwave control |

| Q80 Inspiration | Powertrain |
| --- | --- |
| Petrol engine (VQ30 DDT) | 3.0L V6, petrol |
| Combined engine / motor output: power | 550hp/558PS/410kW |
| Combined engine / motor output: torque | 750Nm/553 lbf/ft |
| Petrol engine induction type | Direct injection, twin turbocharged |
| Petrol engine valves | 24-valve, DOHC, variable valve timing |
| Engine Control Unit (ECU) | Bespoke Infiniti ECU |
| Transmission | 9-speed automatic |
| Drive type | All-wheel drive |
| Acceleration to 60mph | Sub 4 seconds |
| Maximum speed | Electronically limited: 250kph (155mph) |
| Fuel economy | 5.5 L/100km / 42.8 mpg / 18.2 km/L |
| CO2 | 129g/km |

| Q80 Inspiration | Interior highlights |
| --- | --- |
| Seats number / type | Four; individual seating |
| Construction materials | Aluminium / carbon fibre / leather / Alcantara / metal & wood trim |
| Driver technology | Borderless, autonomous customizable system with touch screen interface and hi-res colour HUD |
| Front passenger technology | Borderless, customizable system with hi-res colour HUD |
| Rear passenger technology | Customizable system with colour touch screen for each passenger |
| Lighting | Customizable LED interior mood lighting |
| Audio | Cloud-based, full library audio with bespoke fascia-milled, high sensitivity, low impedance speakers for soundwave control |
| Design flourishes | Rear seat mounted, silver-plated beverage flask |

ENDS

About Infiniti:

Infiniti Motor Company Ltd. is headquartered in Hong Kong with sales operations in approximately 50 countries. The Infiniti brand was launched in 1989. Its range of premium automobiles is currently built in manufacturing facilities in Japan and the United States. Production in China and Europe will start soon along with the expansion of the brand’s portfolio.

As the Title Partner and Vehicle Performance Partner of Infiniti Red Bull Racing, Infiniti has a far-reaching technical collaboration with the Formula One team, and Sebastian Vettel, its four-time World Champion driver, serves as Infiniti’s Director of Performance.

More information about Infiniti, its Total Ownership Experience® and its industry leading technologies can be found at www.infiniti.com. For the latest news on Infiniti in Formula One, visit www.infiniti-gp.com, or follow on Twitter @InfinitiGlobal.

Contacts:

For Infiniti Global Communications, contact:

Matthew Davis

Director, Infiniti Global Communications

Infiniti Motor Company Ltd., Hong Kong

Phone: +852 3948 0127

Mobile: +852 9542 1711

Email: matthew.davis@infiniti.com

Jon Walsh

Senior Manager, Infiniti Global Communications

Infiniti Motor Company Ltd., Hong Kong

Phone: +852 3948 0129

Mobile: +852 9447 9705

Email: jon.walsh@infiniti.com