Embargo: 06:00 20 November 2013

New Porsche Macan unveiled at Los Angeles Auto Show

- World premiere of Porsche Macan – the sixth model line in the Porsche range

- The most dynamic vehicle in the compact sports utility vehicle segment

- Choice of three high performance engines includes two new twin-turbocharged petrol powertrains

- Macan S features a 340 hp 3.0-litre V6  and Macan Turbo a 400 hp 3.6-litre V6

- Option of turbocharged 258 hp diesel – PDK twin-clutch gearbox in combination with all engines

- Active all-wheel drive with Porsche Traction Management standard on all models

- Priced from £43,300 to £59,300 – available to order now, in Porsche Centres from April 2014

Today at the 2013 Los Angeles Auto Show, Porsche celebrates the world premiere of the all-new Macan, a model that sees the German sports car manufacturer expand its range in to a whole new vehicle segment.

Available to order from today, and arriving in Porsche Centres in the UK and Ireland from April 2014, the Macan brings proven Porsche values of maximum acceleration and braking performance, vast engine power, extreme agility and optimum steering precision for the first time to the compact sports utility vehicle (SUV) segment. And all of these features are combined with a high level of comfort and versatility.

The most dynamic vehicle in the compact sports utility vehicle segment

As the first Porsche in the compact SUV segment, the Macan will set new standards in terms of dynamic performance, on both paved streets and uneven terrain. This is because the Macan combines the typical handling characteristics that Porsche has represented right from the outset. The sporting DNA of the Macan, as with all Porsche vehicles, is immediately recognisable in the design, with several styling cues being taken from other Porsche sports cars and then enhanced for the Macan. It is therefore clear to see from the very first glance that the Porsche Macan is the first compact SUV that is also a sports car.

The Macan will be available in three versions from launch. Technical highlights include Porsche Traction Management (PTM) active all-wheel drive and the Porsche PDK double-clutch transmission fitted as standard. The body conceals highly efficient six-cylinder engines, which provide powerful propulsion while achieving favourable fuel consumption figures.

The Macan S is powered by a 3.0-litre V6 bi-turbo engine that delivers 340 hp (250 kW), accelerates from 0 to 62 mph in 5.2 seconds and returns up to 32.5 mpg (NEDC). The 3.6-litre V6 bi-turbo engine in the Macan Turbo produces 400 hp (294 kW) and accelerates the vehicle to 62 mph in 4.8 seconds,

with an average fuel consumption of up to 31.7 mpg (NEDC). With a turbocharged 3.0-litre V6 diesel engine and 258 hp (190 kW), the Macan S Diesel is the long-distance sports car. The engine accelerates from 0 to 62 mph in 6.3 seconds and returns an average of 46.3 mpg (NEDC).

The Macan is a Porsche to its core

Porsche is expanding its range to include a whole new sixth model series. The Macan is the first Porsche model to break into the compact SUV segment and is poised to set new standards in the field of driving dynamics and enjoyment – on both paved streets and uneven terrain. The Macan combines the typical handling characteristics that Porsche has represented right from the outset: maximum acceleration and braking values, vast engine power, extreme agility and optimum steering precision. What's more, all of these features are teamed with a high level of comfort and everyday suitability.

The sporting DNA of the Macan, as with all Porsche vehicles, is also immediately recognisable in the design. The car is unrivalled in its low, broad profile on the road. The wraparound bonnet and gently sloping roof line accentuate the overall impression of sporting elegance and powerful dynamics. Many of the design elements have been taken from other Porsche sportscars and enhanced for the Macan, making it clear to see from the very first glance that the Porsche Macan heralds the first sports car in the compact SUV segment.

The Macan is ‘Made in Germany’, produced at the Leipzig factory. Porsche has invested 500 million Euro in the plant and established an entirely new production line. The line is set up to produce around 50,000 vehicles per year – all manufactured with the utmost precision and to the highest level of quality.

Three models comprise the Macan product range at launch. The Macan S is equipped with a 3.0-litre V6 bi-turbo engine delivering 340 bhp (250 kW) and also features Porsche Traction Management (PTM) active all-wheel drive with an electronically controlled, map-controlled multi-plate clutch. This all-wheel drive is fitted on all Macan models. A seven-speed double-clutch transmission transfers power as required and almost without any interruption in tractive force, enabling acceleration of 0 to 62 mph in 5.4 seconds (or 5.2 seconds with the optional Sport Chrono package fitted). The vehicle reaches a top speed of 158 mph, and its NEDC fuel consumption figures are between 31.4 and 32.5 mpg, which corresponds to CO2 emissions of between 212 and 204 g/km.

The Macan S Diesel is the economical long-distance runner of the three Macan models. Its turbocharged 3.0-litre V6 diesel engine achieves NEDC fuel consumption figures of between 44.8 and 46.3 mpg, which correspond to CO2 emissions of between 164 and 159 g/km. Nevertheless, the Macan S Diesel accelerates from 0 to 62 mph in just 6.3 seconds (or 6.1 seconds with the Sport Chrono package fitted) thanks to its 258 hp (190 kW) engine, and achieves a top speed of 143 mph.

As the top model in the Macan range, the Macan Turbo is set to be the most powerful vehicle in the compact SUV segment. The 3.6-litre V6 bi-turbo engine, which is being used in a Porsche model for the first time, achieves an unrivalled 400 hp (294 kW) and catapults the car from 0 to 62 mph in 4.8 seconds. With the Sport Chrono package fitted, this falls to 4.6 seconds. Although the top speed is 165 mph, the Macan Turbo delivers NEDC fuel consumption figures of between 30.7 and 31.7 mpg, which equates to a CO2 value of between 216 and 208 g/km.

The latest evolution of Porsche Traction Management

Its name comes from the Indonesian word for tiger. And the Macan really does live up to its name: powerful and ready to pounce at any time, yet light-footed and tenacious on off-road terrain.

The sporting all-wheel drive car is ultimately a Porsche invention, designed and first implemented by Ferdinand Porsche in 1900 in the Lohner-Porsche racing car with its four electric wheel-hub motors.

In 1947, Porsche developed the Type 360, better known as the Cisitalia Grand Prix racing car. The car became a true driving legend, not only as a result of its supercharged 12-cylinder engine and consistent lightweight construction, but also thanks to its permanent all-wheel drive. The design was based on the idea that driving torque around bends, or on roads with low grip, can be converted into propulsion more fully and more reliably if all wheels are driven.

The latest stage of evolution of the all-wheel drive – known as Porsche Traction Management (PTM) – has produced one of the world's most powerful drive systems. In launching the Macan, Porsche now offers sporting all-wheel-drive vehicles across an unprecedented range.

A glance at the performance specifications reveals that the Macan has been designed with agility in mind. Further unmistakeable hallmarks of the vehicle include its proportions, design and the large diameter wheels featuring wider tyres on the rear axle than on the front. The engines, drive systems and seven-speed Porsche Doppelkupplung (PDK) bring the dynamic and efficient characteristics of the Macan to the forefront both on and off road, delivering a true Porsche driving experience.

Inside, the driver and passenger seats feature the low position typical of sports cars. The range of equipment fitted on the Macan as standard is extensive, and includes the all-wheel drive, PDK, multi-function sport steering wheel with shift paddles, alloy wheels, high performance audio system and an electrically operated tailgate. The list of optional special equipment offers further highlights, such as the air suspension system, which the Macan brings to this market segment for the first time. There is also Porsche Torque Vectoring Plus (PTV Plus), which has been specially tailored to the Macan. This system distributes varying levels of drive torque to the rear wheels and works in conjunction with an electronically controlled rear-axle differential lock.

The available Porsche options also includes the dynamic high beam forming part of the Porsche Dynamic Light System Plus (PDLS Plus), which continuously adjusts the headlight level in keeping with the traffic ahead and any oncoming vehicles.

Design deeply rooted in the Porsche legacy of sports cars

The sports car heritage of the Macan is evident in many details of its design. The designers have endeavoured to ensure the model's proportions and lines live up to this heritage. The result can be summarised in two words typical of a sports car: broad and low.

The design embodies sportiness, dynamism and precision, together with elegance and lightweight construction. Round lines are combined with strategically positioned precise edges. Its harmonious proportions ensure the Macan appears compact, powerful and close to the road. Even when stationary, design details taken from Porsche sports cars highlight what the Macan has to offer in terms of performance. For instance, the side view window graphics and the sloping roof line at the rear, known at Porsche as the ‘flyline’, are a clear nod to the 911. The rear wheelarches also have the soft profile of the 911.

The 918 Spyder is already regarded as a vehicle that has propelled the Porsche design DNA further forward. The Macan adopts this current DNA: for instance, the basic shape of its main headlights is based on that of the 918 Spyder, while the sideblades at the bottom of the front and rear doors are reminiscent of the lower door seams on the hybrid super sports car. Inside, the Macan is fitted with a multi-function sports steering wheel as standard, the design of which is completely new and based on that in the 918 Spyder.

A true Porsche from all angles

The impressive, assertive front view of the Macan is a distinctive component of the design. The large air intakes are typical of Porsche and highlight the performance class to which the brand's vehicles typically belong. In the Macan Turbo, stylistic elements known as ‘C-blades’ fitted in the air intakes on the right and left of the vehicle accentuate the sporting demeanour and provide a sophisticated aerodynamic solution.

The wraparound bonnet creates an impressive design detail, enclosing the headlights and extending down to the wheel arches. The imposing size of the bonnet and its precision lines running to the front of the vehicle give the Macan a broad and powerful appearance, while the seamless surface of the bonnet presents a clean front to the vehicle.

The side view with its sporting, sloping roof line creates a sharp silhouette and emphasises the dynamic nature of the vehicle, while the design lines running to the rear of the vehicle accentuate the broad, sculpted wings. Together with what are known as the window graphics – the edges of all lateral glass surfaces – and the shape of the D-pillar, these design lines are a further visual reference to the design of the 911.

A further design highlight of the profile, and another means of customising the vehicle, are the sideblades at the bottom of the front and rear doors – these are dynamically formed inserts that are available in different materials as an option. The design of these sideblades is reminiscent of the lower door seams on the 918 Spyder, as is the front door entry guard. Combined with the sophisticated door handles, this makes the doors appear narrower and the sides significantly more sporting and streamlined.

On the Macan S and Macan S Diesel, the sideblades are painted Lava Black as standard. The Macan Turbo features sideblades painted in the same colour as the exterior (optional for Macan S and Macan S Diesel), adding to the classic elegance of its look. Sideblades in Genuine Carbon, available for all models as an option, add extra emphasis to the sporting character of the Macan. A further striking design detail of the Macan is its continuous side sill. Together with the long black roof spoiler, this feature adds to the vehicle's flowing design. The mixed width tyres are up to 265 mm wide on the front axle and 295 mm wide on the rear axle. Combined with alloy wheels of up to 21 inches diameter, the tyres also underline the sporting intent of the Macan.

With its subtle lines and harmonious curves, the rear end fuses sportiness and elegance. It has been consciously designed as a large, mainly undisturbed area to give the vehicle a broader look. To maintain this clean look, the switch for the powerlift tailgate has been concealed at the foot of the windscreen wiper arm, and the number plate is located in the lower valance.

The rear lights on the Macan are another striking feature, boasting an extremely compact three-dimensional design and LED technology – a further reference to the 918 Spyder. On all models, the rear diffuser is flanked on both sides by twin tailpipes – round on the Macan S and Macan S Diesel and square on the Turbo. All models are available with chrome-plated stainless steel sport tailpipes as an option.

Sporting and high-quality interior

The focus on agility continues into the Porsche Macan interior. Sophisticated lines, precise transitions and high-quality workmanship create a harmonious fusion of sportiness, quality and elegance while also subtly and stylishly emphasising the broad stance of the car.

From the low front seats, the sloping centre console, the display and operation concept through to the extensive range of customisation options, the interior offers both a sense of familiarity and striking new features. The driver’s seat features all the character familiar from a sports car. The eye is immediately drawn to the new multi-function sports steering wheel, the design of which is based on the 918 Spyder. Additional multi-function buttons fitted as standard for the telephone, radio and on-board computer, together with the ergonomically-positioned shift paddles, ensure that the drivers' hands are free to stay on the steering wheel and their concentration on the road.

Three round dials with a centrally positioned tachometer combine to form the instrument cluster. The right-hand tube is home to the high-resolution, 4.8-inch colour display. The forward-sloping centre console with the high-set gear selector typical of racing cars draws the driver even further into the cockpit. The buttons for the most important functions are clustered in logical groups on the centre console, allowing for simple and intuitive operation of individual functions.

The standard equipment on the Macan S with the Piano Black interior package and the comfort seats with Alcantara seat trim combine to create an ambience of sportiness and quality. The Macan Turbo is fitted with adaptive sports seats as standard in leather, including 18-way power seats with memory package and a brushed aluminium interior package. In addition, all models are available with the Dark Burl Walnut and Carbon decors as an option.

Engines and drivetrains combining performance and efficiency

Porsche is offering the Macan with three advanced engines. All combine rich torque with impressive power, trademark Porsche qualities. The engines are also highly efficient and environmentally friendly, with all three versions of the Macan meeting the Euro 6 emissions standard. The NEDC fuel consumption figures range from 30.7 mpg (Macan Turbo) to 46.3 mpg (Macan S Diesel).

The Macan Turbo is unrivalled in the compact SUV segment in terms of its driving performance. The 3.6-litre V6 bi-turbo engine unleashes its maximum output of 400 hp (294 kW) at 6,000 rpm. Two turbochargers with a boost pressure of 1.2 bar ensure a powerful intake charge. This power results in acceleration from 0 to 62 mph in just 4.8 seconds and a top speed of 165 mph. The Macan is the first Porsche to feature this engine. The engine is based on a 3.0-litre V6 bi-turbo engine with a stroke that has been increased by 83 mm. All of the dimensions and specifications are based on decades of Porsche experience in developing sport engines.

The Macan S is powered by the new 3.0-litre V6 bi-turbo engine from Porsche. The engine is particularly high-revving, thanks to its 96 mm bore and short 69 mm stroke. When tuning the new engine, the engineers focused on providing uniform performance development and an even torque curve. By combining two turbochargers, positioned in a compact format on the left and the right, which together deliver a boost pressure of 1.0 bar, exceptional performance values have been achieved. The engine reaches its maximum power of 340 hp (250 kW) at between 5,500 to 6,500 rpm. Sprinting from 0 to 62 mph takes just 5.4 seconds and the vehicle reaches a top speed of around 158 mph.

The Porsche VarioCam Plus system in both of the V6 bi-turbo engines ensures that the variable inlet and exhaust camshaft control is continuously and infinitely adjusted, and allows the engine to respond in a flexible manner to the relevant performance requirements. The result is spontaneous acceleration and exceptionally smooth running. The revised direct fuel injection (DFI) concept with multi-hole injectors and a high pressure of 200 bar enables optimum fuel distribution. The jet and taper angles have been optimised with torque, power, fuel consumption and emissions in mind. DFI also improves internal cooling within the combustion chamber as the fuel-air mixture is generated in the cylinder directly. The resulting higher compression ratio provides greater engine power and better engine efficiency. The turbochargers have been specially tailored to the engines and are capable of building up the boost pressure very quickly in response to power requirements.

Integrated dry-sump lubrication and a modified oil sump shape have been developed for the petrol engines destined for use in the Macan. These modifications enable optimum engine lubrication – even in extreme driving situations – and contribute to a particularly low centre of gravity while allowing the ground clearance to be increased. The diesel engine relies on a pressure-fed lubrication concept with a wet sump.

With its turbocharged 3.0-litre V6 diesel engine, the Macan S Diesel is a true long-distance sports car that combines excellent performance with minimum fuel consumption. The 258 hp (190 kW) engine, taken from the Cayenne and subsequently enhanced, has been specially designed for the Macan. It also works perfectly alongside the PDK transmission and is consistent with the vehicle's sports car characteristics.

The high torque of 580 Nm at between 1,750 and 2,500 rpm allows confident acceleration in every driving situation. The vehicle reaches a top speed of 143 mph, accelerating from 0 to 62 mph in 6.3 seconds (or 6.1 seconds with the Sport Chrono package fitted). The optimised common rail fuel injection system enables quiet combustion development while also allowing high turbine speeds within the turbocharger, even at a low engine speed, thereby creates a higher boost pressure. Some of the results of this arrangement include better volumetric efficiency, increased power and more torque. The advanced diesel engine is equipped with a Selective Catalytic Reduction (SCR) system for lower emissions. This system injects a urea solution (AdBlue) into the exhaust gas, and the resulting chemical reaction transforms nitrogen oxides into nitrogen and water.

All Macan models feature an engine with sports car characteristics and they sound like a sports car, too. The sound of the Macan is robust and emotive, indicating that the vehicle is always ready to demonstrate its capabilities on any terrain. As part of the acoustic design, the petrol models include an exhaust flap, in addition to various other components. The flap is map-controlled and load-dependent, which dictates when it opens and shuts.

Power and efficiency in perfect harmony

Performance is not the only attribute of the Macan – maximum efficiency is another one of its defining features. Multiple technologies contribute to the vehicle's low fuel consumption level alongside the standard PDK and the intelligent mix of materials used to construct the Macan. Together, all of these measures result in fuel consumption figures that speak for themselves. The standard automatic Start Stop function shuts off the engine as soon as the Macan brakes to a speed of 1.4 mph – even when the Adaptive Cruise Control (ACC) is activated. When the brake is released, the engine is restarted quickly and smoothly by the system. When drivers lift their foot off the accelerator pedal, the coasting function decouples the engine to allow the vehicle to roll over a longer distance than if the engine was engaged. As soon as the accelerator pedal or brake is actuated again, the PDK selects the appropriate gear and engages the clutch. Up to 1.0 litre of fuel can be saved per 100 kilometres in everyday driving situations.

Electro-mechanical power steering is another of the efficiency technologies in use in the Macan. Thanks to this feature, the electric motor is only supplied with energy if steering action takes place – the advantage for fuel consumption being a saving up to 0.1 litres per 100 kilometres. Depending on the driving situation and cooling requirements, the radiator shutters on the Macan can also be closed – a function that is controlled by the engine management system. Similarly, the underbody shield keeps drag to a minimum by optimising the air flow under the vehicle and reducing turbulence. Electrical system recuperation is another of the efficiency measures featured by the Macan. This concept charges the battery more intensely during the braking and overrun phases. Restricting the charging current of the generator when the battery is fully charged in turn reduces the load on the combustion engine during acceleration phases because the engine does not have to use as much power to charge the battery. In addition, the intelligent thermal management system in the Macan manages the temperature of the engine and transmission to reduce friction losses during the warm-up phase following a cold start. To do this, the thermal flows are managed in a targeted manner and the different coolant circuits are switched on gradually when needed, allowing the engine and transmission to heat up faster.

Porsche Doppelkupplung (PDK) as standard

For the first time in a new Porsche model range, all variants of the Macan feature the high performance

seven-speed Porsche Doppelkupplung (PDK) as standard. The advantages of this transmission design include excellent start-up performance, extremely fast gear changes without any interruption in tractive force, short reaction times, low fuel consumption and outstanding shift comfort. As in virtually all Porsche vehicles that feature the PDK, there are two shifting gates. On the right, the required switching level is engaged via a typical Porsche gear selector, while the left-hand gate can be engaged manually, or with the standard shift paddles on the steering wheel.

In every Macan model, the PDK enables the vehicle to ‘coast’. When driver lifts their foot off the accelerator, the PDK automatically decouples the engaged gear and the vehicles coasts in idle until the required speed is reached. When the accelerator pedal or brake is actuated, the PDK selects the appropriate gear once again and engages the clutch. The PDK contributes to minimum fuel consumption in every Macan and adapts the required driving profile with the help of an intelligent management system.

Active all-wheel drive and Porsche Traction Management (PTM)

Active all-wheel drive is part of the Porsche Traction Management (PTM) system and is standard on all Macan models. Together with the other elements of the system – the electronically controlled, map-controlled multi-plate clutch, the Automatic Brake Differential (ABD) and Anti-Slip Regulation (ASR) – the all-wheel drive monitors traction and safety. PTM has the fastest response time on the market and its design underpins the sports car characteristics of the Macan. The rear axle is always driven, the front axle receives its drive torque from the rear axle, and this torque is dependent on the locking ratio of the electronically controlled multi-plate clutch.

In situations where the rear wheels are on a surface with a significantly lower friction coefficient in comparison to the front axle wheels (for example on ice) which would cause the rear wheels to spin when moving off, up to 100% of the necessary torque can be transferred to the front axle. However, the rear axle is never uncoupled in these situations – instead, 100% of the torque from the rear axle is transferred to the front axle via the multi-plate clutch.

The ASR also reduces wheel spin. Exactly the right amount of propulsion force is transferred to the front wheels on corners to achieve optimum lateral support. Working with the newly developed Porsche Stability Management (PSM) system, the PTM interacts with all systems to secure the appropriate distribution of power for excellent propulsion in every driving situation: on long straights, around tight corners or on surfaces with different friction coefficients. Traction is also improved by the ABD on surfaces with different friction coefficients. If a wheel is in danger of spinning, the PTM brakes the relevant wheel via the ABD and in doing so transfers more drive torque to the other wheel on the same axle.

As a result, the new PTM system not only offers advantages in terms of traction and safety, but it also supports agile driving behaviour for enhanced handling and better dynamism.

Off-road mode at the touch of a button

Off-road mode comes as standard in the Macan, and the function is activated by pressing a button in the centre console at a speed of between 0 - 50 mph. This function switches all the relevant systems to a traction-oriented off-road programme: For example, the shift revolutions and speeds are geared towards a greater level of traction, the clutch is pre-tensioned to a greater degree in order to provide the front axle with the appropriate drive torque more rapidly, and the standard torque split between the front and rear axle as well as the accelerator pedal response are adapted to off-road conditions. Furthermore, the

ground clearance can be increased by 40 mm above its normal level thanks to the optional air suspension, which gives a maximum ground clearance of 230 mm.

Another button in the centre console activates downhill assistance from the Porsche Hill Control (PHC) system. The PHC keeps the vehicle speed constant during descents, and can be adjusted to between 3 and 18 mph.

Option: Porsche Torque Vectoring Plus (PTV Plus)

The Porsche Torque Vectoring Plus (PTV Plus) system has been specially tailored to the Macan in order to improve driving dynamics and driving stability. The PTV Plus uses a variable standard torque split at the rear wheels combined with an electronically-controlled rear axle differential lock. In response to the steering angle, steering speed, accelerator pedal position, yaw rate and vehicle speed, the PTV Plus improves steering behaviour and steering precision through targeted brake interventions on the inside rear wheel to enhance agility. This gives the outside rear wheel a greater propulsion force and enables an additional turning impulse in the steered direction. The result is direct and dynamic steering into the bend. The PTV Plus also makes a positive impact when the Macan is taken off-road. On loose surfaces, rear wheel spin is reduced through targeted locking and braking interventions.

Sport button as standard

Every Macan is fitted with a Sport button as standard, which can be found on the centre console to the left of the gear selector. When the Sport button is pressed, the electronic engine management system makes the engine even more responsive. A touch on the accelerator pedal results in a noticeably more direct response from the engine, the rev-limiter is set to a more specific level and the engine dynamics take on a motorsport feel.

In addition, the PDK enables the shift points to be moved towards the upper speed range, adding an even sportier touch. The response times are shorter, while the gear changes are tighter and instantaneous, particularly for double-clutch downshifts. The engine sound is also adapted to sound even more robust. In addition, the Porsche Active Suspension Management (PASM) chassis control system (part of the standard equipment in the Macan Turbo) is set to sport mode to achieve a more sporting feel for the suspension, and raising agility further.

Option: Sport Chrono package

The optional Sport Chrono package offers improved performance at the push of a button. The Sport Chrono package enables the chassis, engine and transmission to be tuned to an even sportier level, accompanied by a sound that is even more emotive. The Sport Chrono package is characterised by the analogue and digital stopwatch on the dashboard, as well as the additional Sport Plus button in the centre console.

Another element of the package is the performance display on the optional Porsche Communication Management (PCM) system, which provides information on the total driving time, distance travelled around the current lap or the time taken for each lap, for instance. ‘Launch Control’ is also included – this function enables a level of acceleration similar to that required in a racing start. The time advantage gained in a standard sprint from 0 to 100 km/h is 0.2 seconds for all models. ‘Launch Control’ enables improved lap times and a better spread between comfort and responsiveness to achieve a significant boost in driving pleasure.

Chassis, brakes, steering and control systems tuned for urban traffic and off-road driving

The sophisticated chassis of the Porsche Macan illustrates just how much effort has gone into making the vehicle an imposing figure both on and off road. As a sports car, the Macan sets completely new benchmarks for compact SUVs on asphalt. The chassis components, tuning, weight distribution and brakes allow the Macan to take on an exclusive position as the sports car in its segment. No other vehicle in this market can drive on asphalt with such precision and stability, and especially not at high speeds.

The basic geometry of the Macan creates the best conditions for achieving these benchmarks. The low centre of gravity and the wheel base of 2807 mm plus the front track width of 1655 mm and 1651 mm at the rear provide enhanced driving stability, particularly when cornering.

The road performance of the Macan has also been enhanced by its outstanding off-road abilities. The ramp angle of 17.1 degrees (with air suspension at ‘High Level I’: 19 degrees), a ground clearance of 198 mm (230 mm), a front overhang angle of 24.8 degrees (26.6 degrees) and a rear overhang angle of 23.6 degrees (25.3 degrees) also present a consistent message. Overall, the features of the Macan fulfil the exact requirements of many target customers, ie. the perfect performance on the road plus the special reserve capabilities embodied by all-wheel drive and off-road performance.

Three chassis versions for the Macan

There are three chassis versions available for the Macan. The steel spring design fulfils the very highest of standards for performance, driving pleasure, off-roading capabilities and comfort. The consistent lightweight construction philosophy embodied by the aluminium axles and chassis components contributes to driving dynamics and comfort. The front axle is based on a five-link design while the rear axle is formed by a trapezoidal-link design. At the rear axle, the separate arrangement of the springs and dampers on the wheel carrier improves ride comfort and the handling response of the dampers. This arrangement is also responsible for the large loading width of the luggage compartment.

The second version of the Macan chassis is a combination of the steel spring design and the PASM system, which comes as standard in the Macan Turbo top model. The PASM can be selected as an option for the Macan S and the Macan S Diesel. Combining the steel spring design and PASM allows the vehicle to fulfil high standards for long-distance comfort, performance and agility even more successfully. This chassis variant also offers a considerably better spread of the suspension damping across the three PASM programmes of ‘Comfort’, ‘Sport’ and ‘Sport Plus’ at the touch of a button.

Porsche Active Suspension Management (PASM)

The electronically-controlled PASM adjustable shock absorber system increases driving pleasure, safety and comfort and is part of the standard equipment on the Macan Turbo. The system actively and continuously regulates the damper force on the front and rear axles. Vehicles normally demonstrate noticeable body movement in response to a very dynamic driving style involving sharp acceleration and brake phases or when off-roading. The PASM is designed to intervenes and reduce body movement. Depending on their preferences and requirements, drivers can choose between three programmes: ‘Comfort’, ‘Sport’ and ‘Sport Plus’.

Air suspension: Unique in the market segment

The third version of the Porsche Macan chassis, and exclusive in this vehicle segment, is the optional air suspension including levelling system, height adjustment and PASM. This chassis variant also satisfies the highest demands for comfort, sportiness and performance, and puts the vehicle in pole position in comparison to every other chassis design. In comparison to the steel spring design, the Macan with air suspension sits 15 mm lower at Normal Level and, due to the associated lower centre of gravity, it offers both increased driving dynamics and improved comfort. The air suspension maintains a consistent

vehicle position automatically, regardless of the load distribution. The ground clearance can be adjusted to three different levels as required: ‘High Level I’, ‘Normal Level’ and ‘Low Level’. In ‘High Level I’, the vehicle sits 40 mm above ‘Normal Level’, with a maximum ground clearance of 230 mm. This option is activated via the off-road button and can be used at speeds between 0 and 50 mph.

Pressing the PASM button or the Sport Plus button lowers the vehicle by 10 mm to ‘Low Level’. Doing so allows for a maximum ground clearance of 180 mm. Using the ‘Low Level’ setting in combination with Sport Plus mode gets the maximum performance from the Macan, as the centre of gravity is even lower and the PASM is optimised for these conditions.

To allow the luggage compartment to be loaded easily, vehicles fitted with air suspension can be set to loading level, which lowers the rear end to 50 mm below the normal level. Loading level is activated by pressing a button in the luggage compartment.

Powerful brakes offering a top-class performance level

The brakes of the Porsche Macan match the vehicle's exceptional performance level. In line with the usual high Porsche standard, the Macan is leading the way with the most powerful braking system in its market segment. The Macan relies on six-piston fixed-calliper front brakes with aluminium monobloc callipers. In the Macan S and the Macan S Diesel, the brake callipers press on discs with a diameter of 350 mm, while the brake discs in the Turbo have a diameter of 360 mm. In all models, the braking action at the rear is provided by combined floating calliper brakes with an integrated electric parking brake. The rear discs for the Macan S and Macan S Diesel have a diameter of 330 mm and the rear discs of the Turbo have a diameter of 356 mm.

The electric parking brake offers greater comfort and safety when parking the vehicle. The parking brake is released automatically when moving off. Another feature making its debut is the hold function.

Wider rear tyres offering functional and visual benefits

The use of tyres on the Macan is typical of a sports car. The vehicle is designed to use mixed width tyres with different dimensions on the front and rear axles. The mixed tyres emphasise the sports car look of the Porsche Macan and also offer some functional advantages. In combination with the all-wheel drive system designed for tail-heavy vehicles, the wider tyres on the rear axle increase traction and enhance driving stability. The narrower front tyres enable sporting yet precise steering manoeuvres, thereby contributing to the agility of the vehicle, too. Overall, the mixed width tyres play a key role in the excellent driving performance of the Macan. The Macan S and S Diesel features 235/60 R 18 (front) and 255/55 R 18 (rear) tyres, while the Macan Turbo features 235/55 R 19 (front) and 255/50 R 19 (rear) tyres.

The wheels available for the Porsche Macan perfectly capture its character. The range includes rims of up to 21 inches in diameter, which are available for all models. The Macan S and the Macan S Diesel are fitted with the 18 inch diameter ‘Macan S’ wheel as standard, while the 19 inch diameter ‘Macan Turbo’ wheel is available as standard for the Macan Turbo. In addition to these options there are six other wheel designs to choose from, ranging from 18 to 21 inches in diameter. The 18 inch wheels are lightweight forged wheels, while the 19 and 20 inch wheels are produced using flow forming lightweight design technology. The 21 inch wheel is a lightweight forged wheel.

The rolling resistance, typical Porsche performance in terms of handling and braking distance, and weight of all the standard tyres have been optimised. All Porsche Macan models come with Tyre Pressure Monitoring (TPM) as standard. The TPM system increases driving safety and comfort by warning the driver when the tyre pressure is too low or if it detects any rapid drops in pressure. Sensors in all four of the drop-centre rims constantly monitor the air pressure. The driver can check the pressure of all four tyres on the 4.8-inch colour monitor in the central instrument cluster.

Electro-mechanical power steering

The electro-mechanical power steering system – the first to be found in a Porsche SUV – allows the Macan to be driven precisely and more directly with the responsiveness typical of the Porsche brand in all driving situations. The steering system also offers a number of fuel consumption benefits. In comparison to conventional hydraulic steering systems, electromechanical steering saves up to 0.1 litres of fuel per 100 kilometres because the system only requires energy for steering. An important effect of the system is the fact that the Macan can be fitted with a lane departure warning system that works with the

electro-mechanical power steering and controls the active steering interventions when they are necessary.

Body shell developed for the sportscar within the compact SUV segment

A key consideration for the development of the Macan body was the aim to create a vehicle that immediately stood out as a Porsche in comparison to other compact SUVs, ie. to create a sports car for this market segment. This goal is signalled by several of the vehicle's features. For example, the bonnet covers the wheel arches and encloses the main headlights, making the front of the car look broad and robust. The crisp design lines on the bonnet that extend forwards emphasise the width of the vehicle even further. The body is manufactured completely from aluminium, leading to a reduction in weight and therefore contributing to efficiency and dynamism.

The sports car requirements of the Macan played a significant role in the design of the body. The rigidity of the front end is based on the high standards set by the 911 and the Cayman. Thanks to the addition of more bars, this level of rigidity enables optimum driving agility and stability. Another good example is provided by the selective use of materials to achieve a lower centre of gravity. The body platform and doors are manufactured from high and super-high strength lightweight steel sheets, and the bonnet and rear lid are made of aluminium.

With a width of 1923 mm (excluding the exterior mirrors) and a height of 1624 mm, the Macan is a compact and dynamic vehicle. The low centre of gravity and wheelbase of 2807 mm provide enhanced driving stability, particularly when cornering.

These features, combined with a length of 4681 mm (Macan Turbo: 4699 mm), mean that the Macan has the sportiest proportions in its segment. Another distinctive feature of the Macan is the comparatively short overhangs of 924 mm at the front (Macan Turbo: 942 mm) and 950 mm at the rear, which also emphasise its sports car character. The luggage compartment volume is 500 litres, which expands to 1500 litres when the back seats are folded down fully.

No compromises were allowed when it came to the aerodynamic downforce values either: The value at the rear axle is 0.01 negative – guaranteeing high lateral stability even when changing lanes quickly.

Light and wide: The panoramic roof system

As important as it is for the driver to focus on the road, every passenger appreciates being able to glace up to the sky. This is particularly true thanks to the optional, two-part Panoramic Roof System on the Macan, as the front glass element can be uncovered and opened electrically and an electrical roll-up blind dims the entire pane of glass when required.

A sporting seat position

The Macan has a sporting driving position and a more steeply inclined steering column to give it a sports car feel. As a special feature, the front headrests can be adjusted both vertically and longitudinally, while the seat height, seat cushion, backrest angle and the longitudinal position of the standard electrical 8-way comfort seat on the driver's side can also be adjusted. Adaptive sports seats with 18-way adjustment for the driver and front passenger are also available as an option, and are standard on the Macan Turbo.

Optional front seat ventilation is available for even greater seating comfort, with three-stage control

of the ventilation for the seat surfaces and backrests, independently adjustable for both the right and the left seat.

The rear seat system provides space for up to three passengers. The rear seat backrests are split 40:20:40 and can be folded down separately, providing plenty of room for all items of luggage in the luggage compartment.

High level of passive safety

By delivering ideal body rigidity values, the consistent lightweight steel construction makes a key contribution to safety. All elements of the vehicle body shell are designed and connected in such a way that, in the event of a crash, the vehicle structure deforms in a defined manner, thus absorbing the energy from the crash. In addition, super-high-strength steel reinforcements protect occupants in the event of a side impact. High strength and clearly defined deformability are two properties that also come together in the multi-phase steels used.

Multi-collision brake to dissipate kinetic energy

Around a quarter of all accidents resulting in personal injury are ‘multi-collision accidents’, where a second collision follows the first. The multi-collision brake system automatically brakes the vehicle involved in a crash to reduce the residual kinetic energy inherent following the initial collision. The multi-collision brake is triggered when the airbag sensors detect a primary collision, at which point the system initiates maximum braking. The Porsche Stability Management (PSM) system limits this action to a maximum negative acceleration of 0.6 g, thereby ensuring that the driver can maintain control of the vehicle even in the event of automatic braking.

The driver can override the multi-collision brake system at any time. If the system detects that the driver is accelerating, the automatic multi-collision brake is deactivated. The same applies if the driver initiates a full braking manoeuvre at an even higher rate of deceleration. As a general rule, the assistance system brakes until a residual vehicle speed of 6 mph is reached. This residual speed can then be used to drive to a safe location after the braking action.

Outstanding, high-quality equipment inside

The passenger compartment of the Porsche Macan reflects current Porsche sports car design styling cues, delivering a premium appearance. Among the equipment on offer in the interior is the Burmester® High-End Surround Sound system, available for the first time in a vehicle in this segment. Other new equipment options include the lane departure warning system and lane change assist system. Features such as the Adaptive Cruise Control (ACC) with Porsche Active Safe (PAS) deliver a further boost to comfort and safety.

The forward-sloping centre console and the driver's seat position ensure a very short distance between the steering wheel and gear selector, demonstrating how Porsche uses ergonomics to support sporting driving. Furthermore, the driver is now even more closely integrated within the interior thanks to the high-set gear selector typical of racing cars. Controls for all the key functions and settings are clustered in logical groups on the centre console, with buttons located within easy reach to ensure quick, intuitive operation.

The instrumentation is also typically Porsche, offering three conventional round dials with a centrally positioned tachometer. A gear indicator within the tachometer tells the driver which gear has been engaged by the Porsche Doppelkupplungsgetriebe (PDK). A high-resolution, 4.8-inch colour display is contained in the right-hand dial. In addition to the most important on-board computer functions, this feature also displays the maps for the Porsche Communication Management (PCM) system with navigation module where fitted.

Audio systems and Porsche Communication Management (PCM)

Located high up and in the centre of the console, the CDR Plus audio system with Digital radio, which is fitted as standard and features a high-resolution, 7-inch colour touchscreen display, is clearly visible and offers convenient access to a whole host of functions. Features include a universal USB interface for connecting external storage media and end devices, 11 loudspeakers and a total output of 235 watts.

The Porsche Communication Management (PCM) system, which is included as standard in the Macan Turbo, comprises all of the stated CDR Plus functions. In addition, it offers a navigation module with a hard drive, which boasts a capacity of 40 gigabytes, enough for up to 5000 MP3 files, as well as map data for most European countries, including a perspective map view and 3D navigation map.

Burmester® sound system for perfect sound

As the top-of-the-range option when it comes to sound systems, Porsche is also offering a special audio system in the Macan that was developed and made in Germany in cooperation with Burmester®.

Building on the feedback acquired from the systems featured in the Panamera, Cayenne, 911 and Cayman models, this audio upgrade achieves a total output and sound quality that are unparalleled in this class of vehicle. The system comprises 16 individually controlled loudspeakers, including an active subwoofer with a 250 mm diaphragm diameter and an integrated 300 watt Class D amplifier. The total system output is more than 1000 watts.

The Bose Surround Sound system features 14 loudspeakers, including a 200 watt active subwoofer, a total of nine amplifier channels and a total output of 545 watts. The system taps into the sound spectrum of 5.1 digital surround sound recordings. AudioPilot noise compensation technology guarantees a consistent, balanced aural experience, whatever the driving conditions.

Online connection for the PCM via the Aha Radio app

Online features can be accessed in the PCM using the Aha Radio app, available free of charge for Apple and Android devices. This app facilitates use of content such as online radio with personalised web-based music, news feeds, podcasts and audio magazines, as well as weather information and integrated social networks such as Facebook or Twitter. The results of a Google ‘Points of Interest’ search can also be adopted as the navigation destination.

Perfect connection: Porsche Car Connect (PCC)

Porsche Car Connect (PCC) makes it possible to access information and control individual vehicle functions remotely using a smartphone. Corresponding apps are available for both Apple and Android devices. Amongst other functions, the PCC can be used to call up vehicle data and display the vehicle's position, as well as lock the vehicle by activating the central locking system.

If stolen, a vehicle can be located with the help of the Porsche Vehicle Tracking System (PVTS). A separate contract with a service provider recommended by the relevant Porsche partner is required to use Porsche Car Connect. Porsche Car Connect can be supplemented to include the Porsche Vehicle Tracking System Plus (PVTS Plus). This system delivers additional safety measures for the PVTS, such as a plated mounting, shear bolts and two driver authentication keys.

Comfort and safety: assistance systems for the Macan

There are a wide range of assistance systems available for the Porsche Macan. These include the lane departure warning system and lane change assist system, both of which enhance the level of active safety and driving comfort. The reversing camera facilitates reverse parking and manoeuvring and also assists with hitching a trailer. What's more, the ACC system together with PAS supports the driver by emitting visual and audible warnings in dangerous situations, and also initiates an additional brake jolt if required.

Providing support: lane departure warning and lane change assist systems.

The optional lane assist system helps the driver to stay in lane by monitoring the lane markings on both sides of the vehicle by means of a camera. If the vehicle threatens to leave the lane, active steering interventions guide it back on course. The function is activated from speeds of 37 mph and above, and is temporarily deactivated by switching on the indicator. The driver can also activate and deactivate the assist systems independently using a button on the centre console.

The lane change assist system is also available as an option and aids the driver when changing lanes. The system monitors the area behind the vehicle and the blind spot using radar sensors. At speeds of 18 mph or above, the system informs the driver of vehicles approaching quickly from behind or located in the blind spot by providing a visual signal in the exterior mirrors. However, the system does not intervene in the controlling of the vehicle. The function can be activated and deactivated by pressing a button in the driver's door.

Greater comfort and safety: ACC with PAS

To enhance driving comfort and safety in the Macan, Porsche offers ACC with PAS safety function. The ACC function is based on a radar sensor located in the vehicle front end, used to monitor the road up to 200 metres ahead of the vehicle. ACC maintains a speed dependant distance from a vehicle travelling ahead over four pre-selectable stages, and automatically adjusts the driving speed, if necessary down to a halt. This relieves the pressure on the driver, particularly in traffic jams and slow-moving traffic.

PAS builds on this system and can help avoid bumper-to-bumper collisions – even when ACC is switched off. To deliver this function, the front radar system monitors traffic on an on-going basis, looking for vehicles travelling much more slowly up ahead. If the system detects an impending hazard situation, the brake system is preconditioned and the brake assistant is sensitised. If the situation becomes more critical, PAS emits visual and audible warnings, and the driver is alerted to the need to intervene by a jolt in the brake pedal. If the driver responds with an inadequate braking action, the system can increase the brake pressure up to full braking, depending on the situation in question.

Always in view: the speed limit display

The speed limit display is available as an option in conjunction with the PCM system. This minformation system uses a camera to detect speed limits, no overtaking zones and the ends of these zones. The speed limit is displayed to the driver on an on-going basis via the colour screen in the instrument cluster and the PCM screen. When entering a no overtaking zone, information to this effect is also displayed to the driver. If the camera's view is restricted, the system uses the speed information present in the navigation data.

Perfect vision and signals: lighting systems in the Macan

The lighting systems and design of the Porsche Macan form a unified whole, delivering exceptional functionality. The distinctive features at the front of the Macan include the generously proportioned main headlight modules, the daytime running lights and the arrangement of the fog lights. The tail lights with their slim design underscore the vehicle's sports car character, making the Macan unmistakable even in the dark.

Projector-beam halogen main headlights are fitted as standard on the Porsche Macan. Bi-Xenon main headlights are also available as an option (and standard on the Macan Turbo). Also featuring projector type technology, these lights include static and dynamic cornering lights (Porsche Dynamic Light System [PDLS]).

The dynamic cornering light swivels the main headlights towards the inside of a bend, depending on the steering angle and driving speed; the static cornering light activates the auxiliary headlights to illuminate the bend, for example when performing turning manoeuvres.

Control of the driving light is speed-sensitive. This light adjusts the range and contour of the dipped beam at higher speeds for enhanced illumination of the road, for example when travelling on motorways. By dimming the upper light beam in conditions where there is poor visibility, such as fog, the bad weather light can reduce reflection, meaning oncoming drivers are less likely to be dazzled.

The Porsche Dynamic Light System Plus (PDLS Plus) can enhance lighting technology, offering two additional functions: The dynamic high beam variably and continuously adjusts the mlighting range in keeping with oncoming traffic and vehicles travelling ahead. When approaching a crossing, the junction assistant activates the static cornering light on the left and right-hand sides, making the beam of light broader. This improves illumination of the area directly surrounding the vehicle, thereby enhancing safety for both the driver and other road users.

The Macan S and Macan S Diesel feature halogen daytime running lights, while the Macan Turbo is equipped with 4-point LED technology. Fog lights are also included as standard for all Macan models to ensure safety on the road, even in poor weather conditions. The Macan S and Macan S Diesel have round halogen fog lights integrated at the front. On the Macan Turbo, these lights draw on LED technology.

The tail lights are implemented in full using LED technology, and are similar in design to those in the Porsche 918 Spyder. The lights give a highly sophisticated and broad appearance, further reinforcing the sportscar characteristics of the Macan. The 3D design is particularly striking and makes the Macan unmistakable – by day and by night. The circular brake light emphasises the slender details of the horizontal tail light, simultaneously accentuating the direction the 3D light effect, which is just as impressive by day as it is by night, ensures that the vehicle is easily recognisable.

The light comfort package

The optional light comfort package provides pleasant illumination in the vehicle interior. All lights are implemented using LED technology. The package comprises dimmable ambient lighting in the door panels and overhead console, front and back footwell lighting, reading lights in the rear of the vehicle, plus ambient lighting in the exterior mirrors. The make-up mirrors in the sun visors on both the driver's and passenger's side are also illuminated.

The new Porsche Macan in the UK

The Porsche Macan can be ordered from today, and arrives in Porsche Centres in the UK and Ireland from April 2014.

|  |  | UK | Ireland (including VAT & VRT) |
| --- | --- | --- | --- |
| The Macan is available in three models: | Macan S | £43,300 | €76,864 |
|  | Macan S Diesel | £43,300 | €69,741 |
|  | Macan Turbo | £59,300 | €105,266 |

Standard equipment on all models includes Porsche Traction Management (PTM), seven-speed Porsche Doppelkupplung (PDK) double-clutch transmission, alloy wheels, digital radio, front and rear ParkAssist, floor mats, multi-function steering wheel with gearshift paddles, electronic tailgate release, USB port connection and a three-year warranty.

The Macan Turbo adds BOSE Surround Sound audio system, Porsche Communication Management (PCM) with satellite navigation, leather interior, alcantara roof lining, 18-way adjustable adaptive front sports seats with memory, Bi-Xenon headlights with Porsche Dynamic Light System (PDLS), Porsche Active Suspension Management (PASM), sideblades in exterior colour and 19 inch diameter alloy wheels.

Customers will also be able to explore the potential of their new Macan, and further develop their own skills behind the wheel, by participating in a complimentary course at the Porsche Experience Centre, Silverstone.

Technical Data

Specifications of the Porsche Macan S

Body: Self-supporting lightweight body; two-stage driver and front passenger airbags; side and knee airbags for driver and front passenger; head airbags (curtain airbags) at the front and rear; five seats

Aerodynamics: Drag coefficient Cd: 0.36

Frontal area A: 2.61 m2

Engine: Water-cooled 3.0-litre V6 bi-turbo engine; aluminium engine block and cylinder heads; four camshafts; four valves per cylinder; continuous intake camshaft and valve-lift adjustment (VarioCam

Plus); hydraulic valve clearance compensation; direct fuel injection; two turbochargers; integrated dry-sump lubrication; engine oil capacity of 9.5 litres; two three-way catalytic converters each with two oxygen sensors per cylinder bank; electronic ignition with six individual ignition coils; thermal management system

for engine and transmission cooling circuit; variable deceleration fuel cut-off; auto Start Stop function

Bore: 96.0 mm

Stroke: 69.0 mm

Displacement: 2,997 cm3

Compression ratio: 9.8:1

Engine power: 340 hp (250 kW) at 5,500 - 6,500 rpm

Max. torque: 460 Nm at 1,450 - 5,000 rpm

Power output per litre: 113.4 hp/l (83.4 kW/l)

Maximum revs: 6,700 rpm

Fuel type: Super Plus

Electrical system: 12 volts; 3000 W three-phase generator; battery capacity 92 Ah; electrical system

recuperation

Power transmission: Engine and transmission bolted to form one drive unit; active all-wheel drive with electronically controlled, map-controlled multi-plate clutch; seven-speed double-clutch transmission

Gear ratios:

1st gear 3.69

2nd gear 2.15

3rd gear 1.41

4th gear 1.03

5th gear 0.79

6th gear 0.63

7th gear 0.52

R gear 2.94

Front axle final drive ratio 3.88

Rear axle final drive ratio 4.40

Chassis: Front axle: aluminium five-arm wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers

Rear axle: aluminium trapezoidal-wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers

Brakes: Dual-circuit brake system with axle distribution

Front: six-piston aluminium monobloc brake callipers; vented brake discs with a diameter of 350 mm and thickness of 34 mm.

Rear: combined floating calliper brakes with integrated electric parking brake; vented brake discs with a diameter of 330 mm and thickness of 22 mm.

Porsche Stability Management (PSM); vacuum brake booster; brake assistant.

| Wheels and tyres: | Front 8J x 18 with 235/60 R 18 103W |
| --- | --- |
|  | Rear 9J x 18 with 255/55 R 18 105W |
| Weight: | DIN weight empty 1865 kg |
|  | Permissible gross weight 2550 kg |
| Dimensions: | Length 4,681 mm |
|  | Width 1,923 mm |
|  | Width with exterior mirrors 2,098 mm |
|  | Height 1,624 mm |
|  | Wheelbase 2,807 mm |
|  | Track width Front 1,655 mm |
|  | Rear 1,651 mm |

Luggage compartment volume 500 to 1,500 litres

Tank capacity 65 litres

| Performance: | Top speed: 158 mph (254 km/h) |
| --- | --- |
| Acceleration: | 0 - 62 mph (0 - 100 km/h): 5.4 secs (5.2 secs*) |
|  | 0 - 99mph (0 - 160 km/h): 13.2 secs (13.0 secs*) |
|  | 0 - 1000 m: 25.7 secs (25.4 secs*) |
|  | *with optional Sport Chrono package |
| Fuel consumption: | Overall: 31.4 mpg - 32.5 mpg (9.0 - 8.7 l/100 km)* (NEDC) |
|  | Urban traffic: 24.3 mpg - 24.9 mpg (11.6 - 11.3 l/100 km)* |
|  | Extra-urban traffic: 37.2 mpg - 38.7 mpg (7.6 - 7.3 l/100 km)* |
| CO2 emissions: | Overall: 212 - 204 g/km |
|  | Urban traffic: 272 - 264 g/km |
|  | Extra-urban traffic: 179 - 171 g/km |

Emissions class: Euro 6

*Versatility depending on the tyre set used

(NB may vary according to markets)

Specifications of the Porsche Macan Turbo

Body: Self-supporting lightweight body; two-stage driver and front passenger airbags; side and knee airbags for driver and front passenger; head airbags (curtain airbags) at the front and rear; five seats

Aerodynamics: Drag coefficient Cd: 0.37

Frontal area A: 2.61 m2

Engine: Water-cooled 3.6-litre V6 biturbo engine; aluminium engine block and cylinder heads; four camshafts; four valves per cylinder; continuous intake camshaft and valve-lift adjustment (VarioCam Plus); hydraulic valve clearance compensation; direct fuel injection; two turbochargers; integrated dry-sump lubrication; engine oil capacity of 9.5 litres; two three-way catalytic converters each with two oxygen sensors per cylinder bank; electronic ignition with six individual ignition coils; thermal management system for engine and transmission cooling circuit; variable deceleration fuel cut-off; auto Start Stop function

Bore: 96.0 mm

Stroke: 83.0 mm

Displacement: 3,604 cm3

Compression ratio: 10.5:1

Engine power: 400 hp (294 kW) at 6,000 rpm

Max. torque: 550 Nm at 1,350 - 4,500 rpm

Power output per litre: 110.9 hp/l (81.6 kW/l)

Maximum revs: 6,700 rpm

Fuel type: Super Plus

Electrical system: 12 volts; 3000 W three-phase generator; battery capacity 92 Ah; electrical system

recuperation

Power transmission: Engine and transmission bolted to form one drive unit; active all-wheel drive with electronically controlled, map-controlled multi-plate clutch; seven-speed double-clutch transmission.

Gear ratios:

1st gear 3.69

2nd gear 2.15

3rd gear 1.41

4th gear 1.03

5th gear 0.79

6th gear 0.63

7th gear 0.52

R gear 2.94

Front axle final drive ratio 4.13

Rear axle final drive ratio 4.67

Chassis: Front axle: aluminium five-arm wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers.

Rear axle: aluminium trapezoidal-wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers

Brakes: Dual-circuit brake system with axle distribution

Front: six-piston aluminium monobloc brake callipers; vented brake discs with a diameter of 360 mm and thickness of 36 mm

Rear: combined floating calliper brakes with integrated electric parking brake; vented brake discs with a diameter of 356 mm and thickness of 28 mm

Porsche Stability Management (PSM); vacuum brake booster; brake assistant

| Wheels and tyres: | Front 8J x 19 with 235/55 R 19 101Y |
| --- | --- |
|  | Rear 9J x 19 with 255/50 R 19 103Y |
| Weight: | DIN weight empty 1925 kg |
|  | Permissible gross weight 2550 kg |
| Dimensions: | Length 4,699 mm |
|  | Width 1,923 mm |
|  | Width with exterior mirrors 2,098 mm |
|  | Height 1,624 mm |
|  | Wheelbase 2,807 mm |
|  | Track width Front 1,655 mm Rear 1,651 mm |

Luggage compartment volume 500 to 1,500 litres

Tank capacity 75 litres

| Performance: | Top speed: 165 mph (266 km/h) |
| --- | --- |
| Acceleration: | 0 - 62 mph (0 - 100 km/h): 4.8 secs (4.6 secs*) |
|  | 0 - 99 mph (0 - 160 km/h): 11.1 secs (10.9 secs*) |
|  | 0 - 1000 m: 24.2 secs (23.9 secs*) |
|  | *with optional Sport Chrono package |
| Fuel consumption: | Overall: 30.7 mpg - 31.7 mpg (9.2 - 8.9 l/100 km)* (NEDC) |
|  | Urban traffic: 23.4 mpg - 24.5 mpg (11.8 - 11.5 l/100 km)* |
|  | Extra-urban traffic: 36.2 mpg - 37.6 mpg (7.8 - 7.5 l/100 km)* |
| CO2 emissions: | Overall: 216 - 208 g/km |
|  | Urban traffic: 277 - 269 g/km |
|  | Extra-urban traffic: 184 - 176 g/km |

Emissions class: Euro 6

*Versatility depending on the tyre set used

(NB may vary according to markets)

Specifications of the Porsche Macan S Diesel*

Body: Self-supporting lightweight body; two-stage driver and front passenger airbags; side airbags for driver and front passenger; head airbags (curtain airbags) at the front and rear; five seats

Aerodynamics: Drag coefficient Cd: 0.35

Frontal area A: 2.61 m2

Engine: Water-cooled, 3.0-litre V6 turbo diesel engine; grey cast iron crankcase; aluminium cylinder head; four camshafts; four valves per cylinder; hydraulic valve clearance compensation; common rail diesel direct injection (2000 bar) via piezo injectors; one turbocharger; one charge-air cooler; controlled exhaust gas

recirculation with radiator; intake system with map-controlled swirl flap; engine oil capacity of 8.0 litres; emission control system with oxidation catalytic converter, diesel particle filter and Selective Catalytic Reduction (SCR) system; thermal management system; auto Start Stop function

Bore: 83.0 mm

Stroke: 91.4 mm

Displacement: 2,967 cm3

Compression ratio: 16.8:1

Engine power: 258 hp (190 kW) at 4,000 - 4,250 rpm

Max. torque: 580 Nm at 1,750 - 2,500 rpm

Power output per litre: 87.1 hp/l (64.0 kW/l)

Maximum revs: 5200 rpm

Fuel type: Diesel

Electrical system: 12 volts; 2400 W three-phase generator; battery capacity 105 Ah; electrical system

Recuperation

Power transmission: Engine and transmission bolted to form one drive unit; active all-wheel drive with electronically controlled, map-controlled multi-plate clutch; seven-speed double-clutch transmission

Gear ratios:

1st gear 3.69

2nd gear 2.15

3rd gear 1.34

4th gear 0.97

5th gear 0.74

6th gear 0.57

7th gear 0.46

R gear 2.94

Front axle final drive ratio 4.13

Rear axle final drive ratio 4.67

Chassis: Front axle: aluminium five-arm wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers

Rear axle: aluminium trapezoidal-wishbone axle; cylindrical coil springs with internal, hydraulic, twin-tube, gas-filled shock absorbers

Brakes: Dual-circuit brake system with axle distribution

Front: six-piston aluminium monobloc brake callipers; vented brake discs with a diameter of 350 mm and thickness of 34 mm

Rear: combined floating calliper brakes with integrated electric parking brake; vented brake discs

with a diameter of 330 mm and thickness of 22 mm

Porsche Stability Management (PSM); vacuum brake booster; brake assistant

| Wheels and tyres: | Front 8J x 18 with 235/60 R 18 103W |
| --- | --- |
|  | Rear 9J x 18 with 255/55 R 18 105W |
| Weight: | DIN weight empty 1880 kg |
|  | Permissible gross weight 2575 kg |
| Dimensions: | Length 4681 mm |
|  | Width 1923 mm |
|  | Width with exterior mirrors 2098 mm |
|  | Height 1624 mm |
|  | Wheelbase 2807 mm |
|  | Track width Front 1655 mm |
|  | Rear 1651 mm |
|  | Luggage compartment volume 500 to 1500 litres |
|  | Tank capacity 60 litres |
| Performance: | Top speed: 143 mph (230 km/h) |
| Acceleration: | 0 - 62 mph (0 - 100 km/h): 6.3 secs (6.1 secs*) |
|  | 0 - 99 mph (0 - 160 km/h): 16.7 secs (16.5 secs*) |
|  | 0 - 1000 m: 27.2 secs (26.8 secs*) |

*with optional Sport Chrono package

| Fuel consumption: | Overall: 44.8 mpg - 46.3 mpg (6.3 - 6.1 l/100 km)* (NEDC) |
| --- | --- |
|  | Urban traffic: 40.9 mpg – 42.1 mpg (6.9 - 6.7 l/100 km)* |
|  | Extra-urban traffic: 47.8 mpg – 49.5 mpg (5.9 - 5.7 l/100 km)* |
| CO2 emissions: | Overall: 164 - 159 g/km |
|  | Urban: 183 - 176 g/km |
|  | Extra urban: 157 - 150 g/km Emissions class: Euro 6 |

*Versatility depending on the tyre set used

(NB may vary according to markets)